- Smooth quiet motion.

- Complete mechanical synchronization of cycle.

- Positive control of acceleration and speed during full cycle.

- Simple and compact construction.

- Arm with tool grippers automatically locked during rotation.

- Magazine available with 12, 20 or 30 tools.

- Tools taper; ISO 30, ISO 40, ISO 50, HSK, etc

Table of contents ……………………………………………………………………………… Page

Tool changer CUT 	5

General	3

Sequence of cycle motions	3

Directions of rotation of the gripper arm	3

Danger area	3

Danger area	3

Examples of applications	3

Choice of type	3

Mounting instructions	3

Using the self-braking motor	3

Clutch torque limiter	3

Instructions for correct operation	3

Preparation	3

Maintenance	3

Versions	3

Designations of the CUT tool changers	3

Mounting positions of the reduction gear	3

Technical characteristics	3

Overall dimensions   CUT 31	3

Overall dimensions CUT 41	3

Overall dimensions  CUT 51	3

Technical characteristics of the reduction gears	3

Mounting and use of limit switch cams	3

Description of the gripper arm	3

Overall dimensions	3

Type of tool taper	3

Designation of gripper arm  BP	3

Description of the CTM tool magazine.	3

Sequence Diagram	3

Technical characteristics	3

Accessories	3

Overall dimensions  CTM 30	3

Exchange time diagram  CTM 30	3

Designation of the tool magazine  CTM 30	3

Overall dimensions  CTM 40	3

Exchange Time diagram  CTM 40	3

Designation of the tool magazine  CTM 40	3

Overall dimensions  CTM 50	3

Exchange Time diagram  CTM 50	3

Designation of the tool magazine  CTM 50	3

Other versions of the tool change system (places, feeds) as required.	3

Tool change system with chain magazine 	28

Tool change system for drilling work 	29

Disks magazine TM 	30

Product overview 	31

Product overview 	32

- All rights reserved. No part of this catalogue my be duplicated.

- MIKSCH GmbH may make any changes they feel necessary for the improvement of their products without advance notice.

- MIKSCH GmbH may change any market components and accessories mentioned in this catalogue as they feel necessary.

- This catalogue supersedes all earlier ones.

# General

The CUT devices manufactured by Miksch GmbH are mechanical, machine-independent tool change assemblies which, by means of a cam drive, transform an incoming uniform rotary motion supplied by a gearmotor into a regular series of stop-and-go linear and rotary movements of the output shaft onto which the arm of the tool gripper is fixed. The synchronous combination of movements performed by the gripper arm provides the typical tool change cycle which is a characteristic feature of this device.

The design of the product is a simple one: its movements are transformed directly by a mechanical cam and feeler system which controls the acceleration of the intermittent motions and assures positive control throughout the cycle. The main features which are a result of this include accuracy, speed and smoothness of the movements, low vibration and silent operation, versatility in its applications and minimal overall dimensions.

# Sequence of cycle motions

The angle of rotation of the gripper for engaging and releasing the tool is 90° or, on demand, 60°. The tool exchange rotation is 180°. Standard extraction and insertion stroke varies as relevant taper (See Tab.1).

Sequence of the Tool Change cycle

| 1 - Rest position. | 2 - Engaging of the toolholders (rotation of the arm by +60° / +90°), | 3 - Extraction of the toolholders from their couplings (linear downward motion) |
| --- | --- | --- |
| 4 - Exchange of tool positions (arm rotation by +180°) | 5 - Insertion of the exchanged toolholders into their couplings (linear return motion) | 6 - Release of the toolholders (rotation of the arm by -60° / -90°). |

# Directions of rotation of the gripper arm

The STANDARD senses of rotation (designation “D”), is as shown in figure 1 above, i.e. clockwise INPUT shaft motion as shown, produces gripper-arm motion as fig. 1 diagrams 1 through 6.

The OPTION (designation “S”) is for anti-clockwise input shaft motion (as before) to produce gripper-arm motion in the opposite sense.

Directions of rotation

# Danger area

Since it is a positive-action arrangement, the gripper arm moves only within its range. Apart from switching-off, stoppage can occur only owing to an overload of the drive motor, to action by a torque limiter or to breakdown of some internal part.

It is therefore essential not to enter the range of action of the device while it is in operation. When carrying out maintenance, the power must be cut before access to the danger area.

Fig. 3

# Examples of applications

CUT tool-changers can be used for machine tools with vertical-axis spindle as well as with horizontal-axis spindle. Rotation of the grippers to hold the tools (first rotation in the cycle) is clockwise in standard arrangements, but counter-clockwise rotation is available on demand. In this case also the grippers must be suitable for the counter-clockwise direction of rotation. Note: reversing the direction of rotation of the motor means performing the cycle in reverse order, but does not mean actuating gripping in a counter-clockwise direction.

| Vertical machine spindle axis | Horizontal machine spindle axis |
| --- | --- |

Fig. 4

# Choice of type

The size of the CUT depends on the tool taper to be used.

For correct operation one must not exceed the value of size; load; speed shown in the data sheet. Together, these tabulated values determine the maximum torque and force available for the relevant CUT.

If any of these values is exceeded, contact should be taken with our Engineering department to have the device inspected.

# Mounting instructions

The CUT assemblies can be mounted in any orientation, but fill; drain; vent plugs must be repositioned as necessary.

The main plate of the CUT is used with screws to achieve approximate mounting position on the machine. Final accurate position is normally achieved with dowel pins.

# Using the self-braking motor

The self-braking motor is used to stop the mechanism during the mechanical pause (cam dwell period), provided at the end of each tool change cycle, where it will remain until machine control calls for another tool change cycle.

To facilitate adjustment and synchronisation on first mount or maintenance, use of manual brake release and manual drive shaft rotation will be helpful.

# Clutch torque limiter

The CUT assembly standard motor includes worm reduction gear with built-in, externally adjustable, torque limiter, the purpose of which is to eliminate - both during emergency stops and during cycle restart after the emergency - the overload impact caused by inertia of the masses undergoing intermittent motion and therefore to prevent breakage of the mechanical driving parts.

# Instructions for correct operation

Standard CUT assemblies are fitted with an FC3 limit switch-operated detecting unit, a system consisting of 3 limit switches and 3 microcams which control the operations which the machine tool is to carry out during execution of a tool change cycle:

- The adjustment of the microcam which controls motor stopping must be such that the main camshaft stops half-way through the mechanical pause of the CUT assembly.

- The adjustment of the microcam which enables tool release must be such that it occurs at the same time as the interchange arm engages the tools and therefore before extraction starts.

- The adjustment of the microcam which enables tool clamping must be such that it occurs at the same time as the interchange arm has completed insertion of the new tools, but before it releases them.

In order to facilitate these operations, the mechanical cycle of the interchange arm motion includes some brief pauses.

It is also necessary to avoid motor stoppage during motion as it might cause serious damage to the assembly. If a jogging motion is required during synchronising, this must be planned ahead when selecting the machine configuration, for example by allowing such operations to take place only at low speed. It is best to make provision for manual execution of these operations by turning the drive shaft by hand.

Fig. 5

# Preparation

Unless specified otherwise, we supply the CUT devices already filled with long-life lubricant consisting of mineral lubricating oil ISO VG-150. The box is fitted with 2 holes for filling and draining the lubricant. A label is glued to each box to show presence or lack of lubricant. Below some other mineral oil brands which correspond to ISO VG150:

| AGIP BP CASTROL CHEVRON ESSO FINA MOBIL SHELL TOTAL | Blasia 150 Energol GR-XP 150 Alpha SP 150 NL Gear Compound 150 Spartan EP 150 Giran 150 Mobilgear 629 Omala Oil 150 Carter EP 150 | Fig. 6 |
| --- | --- | --- |

When topping up, check that the oil is clean. A fine-mesh filter should be used to pour in the oil. See table 1 for the right amount of oil required for proper lubrication.

# Maintenance

CUT assemblies require very little maintenance. Check the box regularly for oil leakage, always a sign of malfunctioning of the assembly or wear of the seals. If any is noticed, proper maintenance should identify and eliminate the cause.

When carrying out routine servicing, and in any case after 8'000 hours of operation, the CUT assembly gripper shaft should be checked for backlash; if necessary, the whole assembly should be overhauled.

Always ensure that there is unrestricted free airflow for motor cooling purposes, and that such air cannot be contaminated with oil and hence affect the brake.

Check brake wear in accordance with motor manufacturer’s instructions.

# Versions

The tool changers come in the following versions:

VS	CUT with directly driven input shaft (camshaft).

VL	CUT with long input shaft for mounting of standard speed reducer.

VLR	CUT complete with bare shaft input speed reducer and torque limiter.

VLRP	CUT complete with speed reducer (and torque limiter) which is prepared for mounting motor.

VLRA	CUT with self-braking gearmotor and torque limiter

| VS | VL | VLRP | VLRA |
| --- | --- | --- | --- |

Fig. 7

# Designations of the CUT tool changers

The designation of the CUT assemblies consists of sets of alphanumerical characters as in the chart below. Please refer to this chart when ordering, to avoid misunderstandings and delays in deliveries.

| TOOL CHANGER | CUT41 | - | V | - | 90 | - | 110 | - | D | - | VLRA | - | S1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

- Size series

- Spindle axis (V=vertical, O=horizontal)

- Rotation for change arm parking (60° / 90°)

- Shank extraction stroke (110 / 60)

- Sense of rotation of the change arm (D=clockwise, S=counter-clockwise)

- Version

- Mounting orientation of the speed reducer.

EXAMPLE OF DESIGNATION

Of a CUT 41 tool changer for machine tool with SK 40 taper, vertical spindle axis, tool gripping rotation 90° clockwise, with self-braking gearmotor and torque limiter:

CUT41 - V - 90 - 110 - D - VLRA - S1

When ordering, in addition to the position where the reduction gear is mounted, one must also specify all data required to identify the characteristics of the motors. Such data are:

1) The reduction ratio of the worm screw reduction gear and/or cycle time;

2) For VLRP; the size of the IEC B5 motor flange.

3) The specifications of the electric motor: power, polarity, voltage, frequency, etc.

4) The FC3 limit switch assembly, if required.

# Mounting positions of the reduction gear

CUT tool changers can be fitted with a self-braking gearmotor or simply with a worm screw reduction gear. They can be mounted in 6 different positions on the CUT assembly.

| D1 | D3 | D4 |
| --- | --- | --- |
| S1 | S3 | S4 |

Fig. 8

Since the CUT assemblies may be provided with other drive systems than the standard ones, such as combinations of clutch-brake couplings, speed change gears, etc., all dimensional and technical features of these devices must be specified. On demand, these can also be supplied directly by Miksch GmbH.

# Technical characteristics

Tab. 1

| Series | Linear stroke (mm) | Max change arm centres (mm) | Max. tool weight (kg) | Max. stat. torque Ms (N.m) | Max. axial force Fa (N) | Time of cycle (s) | Installed Power (kW) | Lubr. (dm3) | Mass (kg) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| CUT 31 | 85 60 | 600 | 5 | 105 | 600 | See | 0.18 | 4.5 | 38 |
| CUT 41 | 110 60 | 700 | 10 | 215 | 1400 | selection diagrams | 0.37 | 7.2 | 65 |
| CUT 51 | 165 85 | 800 | 20 | 415 | 2100 |  | 0.75 | 13 | 130 |

|  | ACCURACY OF OUTPUT MOVEMENTS Rotation 180° ( 0.05 [deg] Linear stroke 165/60 ( 0.20 [mm] Repeatability ( 0.03 [--] Coplanarity 0.05 [mm] Concentricity 0.05 [mm] |
| --- | --- |

Fig. 9

# Overall dimensions   CUT 31

Version VS

Fig. 10

- The linear 85-mm tool extraction and insertion stroke is the longest achievable; on demand, tool changers with a shorter stroke can be supplied.

- Mounting of the assembly is achieved by the use of the 4 slots in the standard plate, plus two pins added to locate precise final position after having checked that the machine spindle axis and the CUT 31 output shaft are parallel.

- Machine cycle operation is controlled by a set of at least 3 limit switches which are operated by limit switch cams attached to the CUT input shaft.

Version VLRA

Fig. 11

- The linear 85-mm tool extraction and insertion stroke is the longest achievable; on demand, tool changers with a shorter stroke can be supplied.

- Mounting of the assembly is achieved by the use of the 4 slots in the standard plate, plus two pins added to locate precise final position after having checked that the machine spindle axis and the CUT 31 output shaft are parallel.

- As standard, self brake electric worm geared motors are flange mounted directly on the input shaft.

- Machine cycle operation is controlled by a set of 3 limit switches on the external side of the reduction gear.

# Overall dimensions CUT 41

Version VS

Fig. 12

•	The linear 110-mm tool extraction and insertion stroke is the longest achievable; on demand, tool changers with a shorter stroke can be supplied.

•	Mounting of the assembly is achieved by the use of the 4 slots in the standard plate, plus two pins added to locate precise final position after having checked that the machine spindle axis and the CUT 41 output shaft are parallel.

•	Cycle operation must be assisted by a set of at least 3 limit switches which receive the signals from limit switch cams attached to the CUT input shaft.

Version VLRA

Fig. 13

•	The linear 110-mm tool extraction and insertion stroke is the longest achievable; on demand, tool changers with a shorter stroke can be supplied.

•	Mounting of the assembly is achieved by the use of the 4 slots in the standard plate, plus two pins added to locate precise final position after having checked that the machine spindle axis and the CUT 41 output shaft are parallel.

•	As standard, self brake electric worm geared motors are flange mounted directly on the input shaft.

•	Machine cycle operation is controlled by a set of 3 limit switches on the external side of the reduction gear.

# Overall dimensions  CUT 51

Version VS

Fig. 14

- The linear 165-mm tool extraction and insertion stroke is the longest achievable; on demand, tool changers with a shorter stroke can be supplied.

- Mounting of the assembly is achieved by the use of the 4 slots in the standard plate, plus two pins added to locate precise final position after having checked that the machine spindle axis and the CUT 51 output shaft are parallel.

- Cycle operation must be assisted by a set of at least 3 limit switches which receive the signals from limit switch cams attached to the CUT input shaft.

Version VLRA

Fig. 15

- The linear 165-mm tool extraction and insertion stroke is the longest achievable; on demand, tool changers with a shorter stroke can be supplied.

- Mounting of the assembly is achieved by the use of the 4 slots in the standard plate, plus two pins added to locate precise final position after having checked that the machine spindle axis and the CUT 51 output shaft are parallel.

- As standard, self brake electric worm geared motors are flange mounted directly on the input shaft.

- Machine cycle operation is controlled by a set of 3 limit switches on the external side of the reduction gear.

# Technical characteristics of the reduction gears

STM CBF worm screw flanged reduction gear with preset torque limiter

Fig. 16

Tab. 2

| Worm gear reducer STM. CBF LCB. Flange type F1/P | Electric Motor |
| --- | --- |
| Dimensions | Self braking - 4p-V 230/400-Hz 50 |
| Series | A | B | C | Dxl | E | F | G | H | I | L | IEC | kW | O | X | Y |
| CBF40 | 106 | 69 | 49 | 9x30 | 78 | 108 | 59 | 10 | 57 | 7 | 63b | 0.18 | 235 | 123 | 140 |
| CBF50 | 125 | 93 | 60 | 9x30 | 97 | 134 | 69 | 10 | 69 | 9 | 71b | 0.55 | 270 | 138 | 160 |
| CBF70 | 175 | 116 | 66 | 9x30 | 127 | 165 | 93 | 10 | 88 | 17.5 | 80c | 0.95 | 295 | 156 | 200 |

# Mounting and use of limit switch cams

Overall dimensions of the complete FC3 assembly

Fig. 17

Code of the multiple precision limit switch

Balluff  BNS 543-B 03 k 12-61-12, or Euchner  SN 3-R 12-502

As already described in paragraph 11, the cams are mounted in such a way as to actuate the limit switches. Depending on the cycle stage, they control:

1) The release of the tool spindle

2) The clamping of the tool spindle after exchange

3) Stopping of the CUT 41 at end of cycle position

The full cycle is executed with one complete revolution of the camshaft (input shaft) of the CUT.

# Description of the gripper arm

The tool changer gripper arm consists of a central aluminium structure with terminal tool grippers of hardened steel.

Tool gripping and release are obtained by means of a spring-operated mechanism actuated by the rotation of the arm. The latter, in turning, engages or disengages the grippers from the tools when these are in exchange position. While in motion, an irreversible mechanical type safety interlocking device enters automatically into operation and prevents accidental opening of the tool gripper.

The gripper arm is attached to the CUT output shaft by means of a taper compression device which permits easy infinite adjustment and rigid final fixing.

The automatic locking mechanism inside the gripper arm is grease-lubricated and is practically maintenance-free.

The initial positions of the different cycle stages are determined mechanically by the cam of the CUT, so after synchronisation and securing of the gripper on the shaft, the repeatability of the cycle and its positions are absolutely guaranteed.

# Overall dimensions

Gripper arm overall dimensions.

Fig. 18

Tab. 3

| serieS | I | A | B | C | D | E | F | G | H |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 350 | 422 | 250 |  |  |  |  |  |  |
|  | 400 | 472 | 300 |  |  |  |  |  |  |
| BP 30 | 450 | 522 | 350 | 40 | 80 | 33 | 36 | 14 | 40 |
|  | 500 | 572 | 400 |  |  |  |  |  |  |
|  | 550 | 622 | 450 |  |  |  |  |  |  |
|  | 600 | 672 | 500 |  |  |  |  |  |  |
|  | 400 | 480 | 290 |  |  |  |  |  |  |
|  | 450 | 530 | 340 |  |  |  |  |  |  |
| BP 40 | 500 | 580 | 390 | 50 | 100 | 33 | 35 | 14 | 40 |
|  | 550 | 630 | 440 |  |  |  |  |  |  |
|  | 600 | 680 | 490 |  |  |  |  |  |  |
|  | 650 | 730 | 540 |  |  |  |  |  |  |
|  | 500 | 630 | 330 |  |  |  |  |  |  |
|  | 550 | 680 | 380 |  |  |  |  |  |  |
|  | 600 | 730 | 430 |  |  |  |  |  |  |
| BP 50 | 650 | 780 | 480 | 75 | 120 | 33 | 43.5 | 14 | 50 |
|  | 700 | 830 | 540 |  |  |  |  |  |  |
|  | 750 | 880 | 580 |  |  |  |  |  |  |
|  | 800 | 930 | 630 |  |  |  |  |  |  |

# Type of tool taper

Tab. 4

| Type of tool taper | Reference details | Tool changer | Magazine |
| --- | --- | --- | --- |
| J | DIN 69871/69872 | SK 30 | ISO 30 |  |  |
| I | DIN 69893 | HSK - A 32 |  |  |  |
| N | DIN 69893 | HSK - A 40 |  | CUT 31 | CTM 30 |
| T | DIN 69893 | HSK - B 40 |  |  |  |
| X | JIS B6339 | BT 30 |  |  |  |
| A | DIN 69871/69872 | SK 40 | ISO 40 |  |  |
| B | JIS B6339 | BT 40 |  |  |  |
| C | DIN 69893 | HSK - A 50 |  |  |  |
| D | DIN 69893 | HSK - A 63 |  |  |  |
| E | DIN 69893 | HSK - A 80 |  | CUT 41 | CTM 40 |
| F | DIN 69893 | HSK - B 50 |  |  |  |
| G | DIN 69893 | HSK - B 63 |  |  |  |
| H | DIN 69893 | HSK - B 80 |  |  |  |
| L | DIN 69871/69872 | SK 50 | ISO 50 |  |  |
| E | DIN 69893 | HSK - A 80 |  |  |  |
| H | DIN 69893 | HSK - B 80 |  | CUT 50 | CTM 50 |
| P | DIN 69893 | HSK - A 100 |  |  |  |
| U | DIN 69893 | HSK - B 100 |  |  |  |
| Z | JIS B6339 | BT 50 |  |  |  |
| S | Special taper must be identify by the complete identification code. |

# Designation of gripper arm  BP

| CHANGE ARM (gripper arm) | BP 40 | - | D | - | A | - | 450 |
| --- | --- | --- | --- | --- | --- | --- | --- |

- Size series

- Direction of rotations

D=Clockwise

S=Counterclockwise

- Type of taper (A,....,H  See table par. 28)

- Distance between grippers

EXAMPLE: Gripper arm for SK 40 taper with gripper distance 450 mm

GRIPPER ARM BP 40 - D - A - 450

# Description of the CTM tool magazine.

The tool magazine consists of:

- 1 CUT VLRA tool changer (modified)

- 1 gripper arm complete with tool grippers with automatic lock during rotation

- 1 cam indexing table type either RIGIDIAL or IR

- 1 rotary tool magazine with 12, 20 or 30 tools

Description of operation

The rotary disc magazine comprises an indexing plate which carries the plastic tool cells. Any cell can be tilted through 90° degrees by a pneumatic cylinder, when it is in the tool change position.

Indexing of the magazine is achieved by an indexing table and can be either clockwise or counter-clockwise so that the search for the tool selected and its positioning can be carried out following the shortest route. The direction of rotation of the magazine is reversed by reversing the direction of rotation of the motor of the INDEXING table.

Recognition of the tool magazine position and consequently of the tool selected is obtained by means of limit switches and appropriate mini-cams located on the tool plate. The number of indexes of the index table, and hence the particular tool, is controlled by a limit switch operating at the cam dwell period of the index table.

The CUT tool changer is assisted in its cycle by a multiple 3-way limit switch. See paragraph 11.

To safeguard the mechanisms, the gearmotors controlling the CUT tool changer and the CTM tool magazine have a built-in torque limiter. The drives are achieved using only simple 3-phase asynchronous self-braking motors.

# Sequence Diagram

(The strokes and the times vary as a function of the magazine)

Fig. 19

Indexing time

t1=Indexing time of the magazine between 2 adjacent tools	t5=Rotation of the gripper arm to interchange the tools

t2=Drop-down tilting of the tools	t6=Up-stroke to insert the tools

t3=Rotation of the gripper arm from park to collect tools	t7=Rotation of the gripper arm from release to park

t4=Down-stroke to extract the tools	t8=Lift-up of the tool into magazine

# Technical characteristics

Tab. 5

| CTM |  | 30 | 40 | 50 |  | CTM |  | 30 | 40 | 50 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Max tool weight | [kg] | 5 | 10 | 20 |  | Max tool exchange centres distance | [mm] | 550 | 650 | 800 |
| Max total tool weight |  |  |  |  |  | Min exchange time | [s] | 1,3 | 1,5 | 1,5 |
| 12 tools | [kg] | 60 | 160 | 200 |  | Time to rotate magazine between adjacent tool positions | [s] | 0,6 | 0,6 | 0,85 |
| 20 tools | [kg] | 80 | 160 | 200 |  | from tool to tool | [s] | 0,85 | 0,85 | 1 |
| 30 tools | [kg] | 80 | 160 | 300 |  | Max tool search time: |  |  |  |  |
| Max tool diameter |  |  |  |  |  | 12 tools | [s] | 4 | 4 | 6,5 |
| 12 tools | [mm] | 90 | 100 | 150 |  | 20 tools | [s] | 6 | 6 | 8,5 |
| 20 tools | [mm] | 60 | 90 | 120 |  | 30 tools | [s] | 10,5 | 10,5 | 15 |
| 30 tools | [mm] | 60 | 80 | 120 |  | Tool changer motor rating | [kW] | 0,18 | 0,37 | 0,75 |
| Max tool diameter with |  |  |  |  |  | Magazine motor rating | [kW] | 0,13 | 0,18 | 0,75 |
| adjacent slots empty |  |  |  |  |  | Tilting pneumatic cilinder |  |  |  |  |
| 12 tools | [mm] | 170 | 190 | 290 |  |  |  |  |  |  |
| 20 tools | [mm] | 120 | 180 | 240 |  | Diameter | [mm] | 32 | 40 | 63 |
| 30 tools | [mm] | 160 | 165 | 240 |  | Stroke | [mm] | 40 | 50 | 75 |
| Min tool exchange centres distance | [mm] | 350 | 400 | 500 |  | Minimum feed pressure | [bar] | 5 | 5 | 5 |

# Accessories

The CTM rotary magazine can be supplied with a manual system for extracting the tool from the pockets; the same system is also used to assist manual insertion of the tool into the magazine pockets. A limit switch indicates the correct insertion and extraction position.

Extraction of the tool from the pocket by means of manual system can be carried out in one position only.

Terminal block
On demand, the tool changer can be prewired to a terminal block with numbered terminals.

Pneumatic connection
A complete pneumatic connection assembly can be provided.

Fig. 20

# Overall dimensions  CTM 30

Fig. 21

Tab. 6

| TYPE | N° | F (extraction stroke) | A | B | C | D | E | K | Weight |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | OF TOOLS | ISO SK 30 | HSK |  |  |  |  |  |  | (kg) |
| CTM 30/12 | 12 |  |  | 215 | 160 | 350 | 430 | 380 | 320 | 105 |
| CTM 30/20 | 20 | 85 | 60 | 240 | 185 | 400 | 480 | 405 | 320 | 115 |
| CTM 30/30 | 30 |  |  | 355 | 300 | 630 | 710 | 520 | 370 | 130 |

Tab. 7

| Distances I | 350 | 400 | 450 | 500 | 550 |
| --- | --- | --- | --- | --- | --- |
| G | 180 | 205 | 230 | 255 | 285 |

# Exchange time diagram  CTM 30

N.B. : “ In the case of positioning the CUT with horizontal axis and in the presence of loads highly unbalanced; do not consider the data applied on the chart, but contact our technical office.”

Fig. 22

Example: Tool weight 1 [kg], exchange distance 550 [mm], can be changed in an exchange time of 2.57 [s]

# Designation of the tool magazine  CTM 30

The designation of the CTM assemblies consists of sets of alphanumerical characters as in the chart below. Please refer to this chart when ordering, to avoid misunderstandings and delays in deliveries.

| TOOL MAGAZINE | CTM 30 | - | D | - | V | - | 20 | - | J | - | 550 | / | 2.57 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

- Size series

- Rotation of the tool changer arm

D = Clockwise (STANDARD)

S = Counter-Clockwise

- Tool machine spindle axis orientation

V = vertical

O = horizontal

- No. of tools in the magazine  ( Standard  12 - 20 - 32 )

- Type of taper  ( J - I - N - T - X - M )  See Tab.4, Page 16

- Exchange distance ( Standard 350 - 400 - 450 - 500  -550 [mm] )

Exchange time with 50Hz motor  ( 1.30 - 1.90 - 2.57 - 3.60  [s] )

Exchange time with 60Hz motor  ( -.---  - 1.60 - 2.20 - 3.00  [s] )

EXAMPLE OF DESIGNATION

For a magazine with 20 tools on a machine with ISO 30 taper, vertical spindle axis, tool gripping rotation clockwise, with self-braking gearmotor and torque limiter. Gripper with 550 (mm) exchange distance and 
2.57 (s) exchange time.

CTM 30 - D - V - 20 - J - 550 / 2.57

# Overall dimensions  CTM 40

Fig. 23

Tab. 8

| TYPE | N° | F (extraction stroke) | A | B | C | D | E | K | Weight |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | OF TOOLS | ISO SK 40 | HSK |  |  |  |  |  |  | (kg) |
| CTM 40/12 | 12 |  |  | 250 | 155 | 400 | 510 | 556 | 360 | 165 |
| CTM 40/20 | 20 | 110 | 60 | 350 | 255 | 600 | 715 | 446 | 360 | 190 |
| CTM 40/30 | 30 |  |  | 460 | 365 | 820 | 930 | 554 | 475 | 235 |

Tab. 9

| Distances I | 400 | 450 | 500 | 550 | 600 | 650 |
| --- | --- | --- | --- | --- | --- | --- |
| G | 210 | 235 | 260 | 285 | 310 | 335 |

# Exchange Time diagram  CTM 40

N.B. : “ In the case of positioning the CUT with horizontal axis and in the presence of loads highly unbalanced; do not consider the data applied on the chart, but contact our technical office.”

Fig. 24

Example: Tool weight 4 [kg], exchange distance 580 [mm], can be changed in an exchange time of 2.24 [s]

# Designation of the tool magazine  CTM 40

The designation of the CTM assemblies consists of sets of alphanumerical characters as in the chart below. Please refer to this chart when ordering, to avoid misunderstandings and delays in deliveries.

| TOOL MAGAZINE | CTM 40 | - | D | - | V | - | 20 | - | A | - | 580 | / | 2.24 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

- Size series

- Rotation of the tool changer arm

D = Clockwise (STANDARD)

S = Counter-Clockwise

- Tool machine spindle axis orientation

V = vertical

O = horizontal

- No. of tools in the magazine  ( Standard  12 - 20 - 32 )

- Type of taper  ( A - B - C - D - E - F - G - K )  See Tab.4, Page 16

- Exchange distance ( Standard 350 - 400 - 450 - 500 - 580 [mm] )

Exchange time with 50Hz motor  ( 1.48 - 1.62 - 2.24 - 2.96 - -.---   [s] )

Exchange time with 60Hz motor  ( -.---  - 1.35 - 1.87 - 2.47 - 3.48  [s] )

EXAMPLE OF DESIGNATION

For a magazine with 20 tools, on a machine with ISO 40 taper, vertical spindle axis, tool gripping rotation clockwise, with self-braking gearmotor and torque limiter. Gripper with 580 (mm) exchange distance and 2.24 (s) exchange time.

CTM 40 - D - V - 20 - A - 580 / 2.24

# Overall dimensions  CTM 50

Fig. 25

Tab. 10

| Type | N° OF TOOLS | F (extraction stroke) | A SK 50 | A HSK | B | C | D | E | K | U | Weight [kg] |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | SK50 | HSK |  |  |  |  |  |  |  |  |  |
| CTM 50/12 | 12 | 165 | 85 | 379 | 391 | 315 | 600 | 750 | 500 | 233 | 130 | 350 |
| CTM 50/20 | 20 |  |  | 479 | 491 | 415 | 800 | 950 | 600 | 267 | 120 | 450 |
| CTM 50/30 | 30 |  |  | 679 | 691 | 615 | 1200 | 1350 | 800 | 267 | 125 | 550 |

Tab. 11

| Distances I | 500 | 550 | 600 | 650 | 700 | 750 | 800 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| G | 280 | 305 | 330 | 355 | 380 | 405 | 430 |

# Exchange Time diagram  CTM 50

N.B. : “ In the case of positioning the CUT with horizontal axis and in the presence of loads highly unbalanced; do not consider the data applied on the chart, but contact our technical office.”

Fig. 26

Example: Tool weight 15 [kg], exchange distance 700 [mm], can be changed in an exchange time of 3.00 [s]

# Designation of the tool magazine  CTM 50

The designation of the CTM assemblies consists of sets of alphanumerical characters as in the chart below. Please refer to this chart when ordering, to avoid misunderstanding and delays in deliveries.

| TOOL MAGAZINE | CTM 50 | - | D | - | V | - | 20 | - | L | - | 700 | / | 3.00 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

- Size series

- Rotation of the tool changer arm

D = Clockwise (STANDARD)

S = Counter-Clockwise

- Tool machine spindle axis orientation

V = vertical

O = horizontal

- No. of tools in the magazine  ( Standard  12 - 20 - 30 )

- Type of taper  ( L - E - H - P - U - Z - R )  See Tab. 4, Page 16

- Exchange distance ( Standard 500 - 550 - 600 - 650  -700 - 750 - 800 [mm] )

Exchange time with 50Hz motor  ( 2.25 - 3.00 - 4.20 [s] )

Exchange time with 60Hz motor  (2.50 - 3.50 - 5.10 [s] )

EXAMPLE OF DESIGNATION

For a magazine with 20 tools, on a machine with admission SK 50, vertical spindle axis, tool gripping rotation clockwise, with self-braking gearmotor and torque limiter, tool weight 15 kg, standard gripper with 700 (mm) exchange distance and 3.00 (s) exchange time.

CTM 50 - D - V - 20 - L - 700 / 3.00

Short description

| CTA | 50 D 0 50 L 500 / 3.00 |
| --- | --- |

TYPE									      Change time

Series								     	      Axis distance

Grab rotation direction							     Feed type

Spindle									Tool places

| Description of the change system | A | B |
| --- | --- | --- |
| CTA 50 / 40 (40 tools) | 2720 | 2080 |
| CTA 50 / 50 (50 tools) | 3370 | 2730 |
| CTA 50 / 60 (60 tools) | 4020 | 3380 |
| CTA 50 / 70 (70 tools) | 4800 | 4160 |

Note:		It is possible to attach the tool changer at any cassette position, except the cassettes

marked with an *.

Other versions of the chain magazine (places, feeds) as required.

Technical data

| Tool feed | : SK 50 DIN 69871 (HSK 100 - HSK 160) |
| --- | --- |
| Number of tools | : 30 - 80 tools |
| Grab arm axis distance | : 700 - 850 mm |
| Max. tool weight | : 25 kg |
| Tool change time | : 2.25 s – 6 s |
| Speed of the displacement device | : 30 m/s |
| Max. Ø (dia.) of the tools | : 120 mm |
| Max. Ø of the tools with adjacent empty place | : 200 mm |
| Magazine switching time | : 0.85 s |

# Other versions of the tool change system (places, feeds) as required.

Disc magazine TM 40 / 24 with 24 places for HSK-A63

Max. tool diameter:	106 mm

Tool diameter with adjacent empty place:	210 mm

Max. tool weight		12 kg

Max. weight of all tools		160 kg

Other versions of the chain magazine (places, feeds) as required.

CTA

CTNR

Pallet exchanger CPS (Component pallet exchanger)

CTM 40 - Tool changing system combined with Linear unit SMC 100

# Text boxes

N° 4 Holes M12

Spindle axis

Viewed from A

N° 3 Holes Ø10H7

Spindle axis

Viewed from A

Viewed from A

N° 2 Holes Ø12H7

N° 9 Holes M12

Fig. 1

Fig. 2

232

Stroke 85

43,75

98

Stroke 110

113

62,5

602

Ø 156

Stroke 165

166

N° 6 Holes M12

N° 3 Holes Ø12H7

I (Standard) = 500 - 550 - 600 - 650 - 700 - 750 - 800

Counter-clockwise rotation

Clockwise rotation

The fixing feet can adjusted as desired apart from to where they would only with the space for assembling the tool changer